## Slide 1
Notes: https://www.fortinet.com/training-certification

## Slide 3
https://www.fortinet.com/products/fortigate/fortiasic
Notes: https://www.fortinet.com/products/fortigate/fortiasic

## Slide 4
Notes: Zero Trust

## Slide 5
History OF Firewall
The Seven Layers of the OSI Model are:
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer
Notes: https://www.thepcinsider.com/who-invented-firewall-history-evolution-types-generations/

## Slide 6
History OF Firewall
Evolution, History, Types, and Generations of the various Firewall Technologies
1988 – First Generation – Packet-Filter Firewall (Stateless Firewalls)
This type of firewall does not look at the connection state of the packet. Thus, it doesn’t maintain a state
1989 – Second Generation – Stateful Firewall
A Stateful Firewall keeps information about the active sessions and connection states; it records all connections passing through it.
1991 – Third Generation – Application Layer Firewall
2004 – IDC coins the term Unified Threat Management (UTM)
It is the evolution of the traditional firewall into a comprehensive network security solution. A UTM uses technologies such as Network Firewall, Web Filtering, Gateway Antivirus, Intrusion Prevention System (IPS), Anti-Spam, VPN, etc. to protect networks from threats.
2009 – Gartner defines the Next-Generation Firewall (NGFW)
Notes: https://www.thepcinsider.com/who-invented-firewall-history-evolution-types-generations/

## Slide 7
History OF Firewall
Notes: https://www.thepcinsider.com/who-invented-firewall-history-evolution-types-generations/

## Slide 8
History OF Firewall
Notes: https://www.thepcinsider.com/who-invented-firewall-history-evolution-types-generations/

## Slide 9
UTM vs NGFW
UTM are usually bundled feature set, NGFW has bundle but licensing can be selective.
a UTM consolidates many security functions (email security, AV, IPS, URL filtering etc.) and is tailored mostly to SMBs in terms of management capabilities, throughput, support, etc.
A NGFW is an enterprise-grade product that at the very least includes IPS capabilities and application awareness (layer 7 control).
At Fortinet, for example, we offer customers the ability to deploy a FortiGate device as a pure firewall, an NGFW (enabling features like Application Control or User- and Device-based policy enforcement) or a full UTM (enabling additional features like gateway AV, WAN optimization, and so forth).
https://www.fortinet.com/support/support-services/fortiguard-security-subscriptions/fortigate-security-bundles
Notes: https://www.algosec.com/blog/state-of-the-firewall-utm-vs-ngfw/

## Slide 10
UTM

## Slide 11
Next-Generation Firewall (NGFW) is the part of the third generation in firewall technology, combining a traditional firewall with other network device filtering functionalities, such as an
application firewall using an in-line deep packet inspection system (DPI), an intrusion prevention system (IPS).

## Slide 15
https://www.fortinet.com/products/fortigate/fortiasic

## Slide 17
FortiGate Series and Models
https://www.fortinet.com/products/next-generation-firewall

## Slide 20
Notes: Transparent vs Routed

## Slide 21
Notes: Transparent vs Routed

## Slide 22
NAT Mode

## Slide 23
Transparent Mode

## Slide 24
Transparent Mode
config system settings
set opmode transparent
set manageip <address and netmask>
set gateway <address>
end

## Slide 25
Transparent Mode
Don’t have IP address
Work as a layer 2 switch
No NAT
No Routing
Inspection traffic until layer 2

## Slide 28
System -- > FortiGuard

## Slide 32
Using GUI

## Slide 33
Config : Use the config commands to change your FortiGate's configuration.
Execute : perform immediate operations on the FortiGate unit
- execute ping , traceroute …
- execute reboot , shutdown
- execute ha ..
- execute update-now
Get : get commands retrieve information about the operation and performance of your FortiGate unit
Show :
Diagnose :like Debug in cisco

## Slide 34
config system interface
edit port1
set ip 192.168.1.99/24
set allowaccess http https ping ssh telnet
end
config system route
edit 1
set device port1
set gateway 192.168.1.1
end

## Slide 38
NTP (Network time Protocol) & PTP (Precision time Protocol )
NTP provides millisecond accuracy while PTP provides sub-microsecond accuracy.

## Slide 39
NTP (Network time Protocol) & PTP (Precision time Protocol ) (Cont)
NTP server:
config system ntp
set ntpsync enable
Set type custom
config ntpserver
edit 1
set server 192.168.1.1
Setup device as local NTP server
Enable to configure the FortiGate as a local NTP server. This option is not available if Set Time is PTP.
In the Listen on Interfaces field, set the in

## Slide 40
DNS
With DNS, FortiGate can connect to the FortiGuard network

## Slide 45
Where to Apply 2FA/MFA
VPN users : SSL/Ipsec
Admin users

## Slide 49
maximum number of logged-in administrators
FGT# config system global FGT(global) # set admin-login-max ? please input integer value (1-100) FGT(global) # set admin-login-max 1 FGT(global) # end

## Slide 51
Notes: https://docs.fortinet.com/document/fhttps://docs.fortinet.com/document/fortigate/7.2.8/administration-guide/574723/interface-settings#Configurortigate/7.2.8/administration-guide/574723/interface-settings#Configur

## Slide 52
Fortitelemetry is the protocol used for information sharing between Fortinet devices within the security fabric. The security fabric is a way of devices integrating and sharing information to provide a wholistic view of the network and events within it.
For instance, if a user gets an email with zero to Fortisandbox for a ready malware, Fortimail can send the attachment result, Fortisandbox will discover that it is malicious tell the Fortimail to quarantine the file, but then ALSO it will tell every Fortigate and FortiClient in the environment (through Fortitelemetry) about the malicious file, ensuring that the file is quarantined everywhere in the network, even if a user did somehow get the file. You also can setup automated actions, such as quarantining an endpoint if a compromise is discovered, which would take place across the entire fabric, regardless of where the user is located.

## Slide 53
Secure your admin account
Two Factor Authentication
Trusted Host
Notes: https://www.youtube.com/watch?v=hKX87Kc53NU

## Slide 55
Configuration save mode
Notes: https://www.youtube.com/watch?v=hKX87Kc53NU

## Slide 56
Config sys admin
Edit admin
Set password admin2

## Slide 57
Note:
Starting with FortiOS 7.2.4 the maintainer account was removed, meaning this method to reset a password will no longer work. Users must instead have physical access to the FortiGate and perform a TFTP restore of the firmware in order to regain access to the FortiGate.

## Slide 61
Interfaces in Transparent Mode
Only configure through CLI
config system settings
set opmode transparent
set manageip <mng_ip>/<netmask>
set gateway <gateway_ip>
end

## Slide 66
Aggregation and redundancy
Link aggregation (IEEE 802.3ad) enables you to bind two or more physical interfaces together to form an aggregated (combined) link. This new link has the bandwidth of all the links combined. If a link in the group fails, traffic is transferred automatically to the remaining interfaces. The only noticeable effect is reduced bandwidth.
This feature is similar to redundant interfaces. The major difference is a redundant interface group only uses one link at a time, where an aggregate link group uses the total bandwidth of the functioning links in the group, up to eight (or more).
An interface is available to be an aggregate interface if:
It is a physical interface and not a VLAN interface or subinterface.
It is not already part of an aggregate or redundant interface.
It is in the same VDOM as the aggregated interface. Aggregate ports cannot span multiple VDOMs.
It does not have an IP address and is not configured for DHCP or PPPoE.
It is not referenced in any security policy, VIP, IP Pool, or multicast policy.
It is not an HA heartbeat interface.

## Slide 67
Aggregation and redundancy
LACP 802.3ad tra due firewalls fortigate e due nexus in vpc cisco
Notes: https://www.ingegnerianetworking.com/switching/l2-config/lacp-802-3ad-tra-due-firewalls-fortigate-e-due-nexus-in-vpc-cisco

## Slide 68
Interface with reference
You can’t delete any interface reference to route and policy

## Slide 69
LAB
Link aggregation between cisco and Fortigate

## Slide 70
Cases
Link aggregation between cisco and Fortigate
- Server -- SW
- SW - SW
- Router -- SW
- FW -- SW

## Slide 71
Vlan Interface (Sub-Interface)

## Slide 72
LAB
Use Fortigate as inter vlan routing

## Slide 73
FortiLink
FortiLink defines the management interface and the remote management protocol between the FortiGate and FortiSwitch.

## Slide 74
Hardware Switch
https://docs.fortinet.com/document/fortigate/7.2.5/administration-guide/100999

## Slide 75
Software Switch Switch
https://docs.fortinet.com/document/fortigate/7.2.5/administration-guide/277799/software-switch

## Slide 76
Loopback interface
A loopback interface is a logical interface that is always up. Its IP address does not depend on one specific physical port, and the attached subnet is always present in the routing table. Therefore, it can be accessed through several physical or VLAN interfaces.
Typically, a loopback interface can be used with management access, BGP peering, PIM rendezvous points, and SD-WAN.
# use with BGP routing
# Fortigate behind Cisco Router
# public ip subnet

## Slide 77
Virtual Wire
# Two interface don’t have IP address and are treated like a similar to transparent mode
# All traffic received by one interface in virtual wire pair can only be forwarded out to other
# need a virtual Wire pair policy
# Virtual Wire Pairing can be used for Fortigate in both the NAT and Transparent
# A virtual wire pair can include redundant and 802.3ad aggregate (LACP) interfaces.

## Slide 78
You can also use the one-arm sniffer to configure the FortiGate to operate as an IDS appliance to sniff network traffic for attacks without actually processing the packets. To configure a one-arm IDS, enable sniffer mode on a physical interface and connect the interface to the SPAN port of a switch or a dedicated network tab that can replicate the traffic to the FortiGate.
Traffic scanned on the one-arm sniffer interface is processed by the CPU, even if there is an SPU, such as NPU or CP, present. The one-arm sniffer may cause higher CPU usage and perform at a lower level than traditional inline scanning, which uses NTurbo or CP to accelerate traffic when present.
The absence of high CPU usage does not indicate the absence of packet loss. Packet loss may occur due to the capacity of the TAP devices hitting maximum traffic volume during mirroring, or on the FortiGate when the kernel buffer size is exceeded and it is unable to handle bursts of traffic.

## Slide 80
VDOM
Virtual Domains (VDOMs) are used to divide a FortiGate into two or more virtual units that function independently.
By default, most FortiGate units support 10 VDOMs, and many FortiGate models support purchasing a license key to increase the maximum number.
FortiGate-VM V-series, S-series, and Flex-VM instances support split-task VDOMs without any additional VDOM licenses.

## Slide 81
VDOM
Routing Table also separated . Interfaces are separated

## Slide 82
VDOM : CLI changes

## Slide 83
VDOM : administration

## Slide 84
VDOM : use cases
physical FortiGate unit requires a FortiGuard license to access security updates. VDOMs do not require any additional FortiGuard licenses, or updating — all the security updates for all the VDOMs are performed once per update at the global level
Fw as a service
Edge and DC FW at the same Hardware
NAT and Transparent

## Slide 85
How to Configure Inter-VDOM links

## Slide 89
LAB
DHCP relay

## Slide 97
Restore config
Should use the same model

## Slide 98
Restore config
With vdom

## Slide 99
Fortigate Auto backup script
config system auto-script
edit backup
set interval 120
set repeat 0
set start auto
set script “execute backup config tftp backup5.conf 192.168.1.1 “
end
Notes: https://community.fortinet.com/t5/FortiGate/Technical-Tip-Automated-script-execution/ta-p/193685
https://docs.fortinet.com/document/fortigate/7.0.1/administration-guide/780930/configuration-scripts
https://docs.fortinet.com/document/fortigate/7.0.1/administration-guide/530847/workspace-mode

## Slide 100
Automatic Configuration Backup after each logout
FW# config system global FW# set revision-backup-on-logout enable FW# end
Notes: https://itadminguide.com/fortigate-cli-commands-for-troubleshooting/

## Slide 102
With VDOM

## Slide 104
- Always read the release note
- Take Backup
- Some issues with upgrade :
Loss connection with FortiAP
Loss connection with FortiSwitches
SDWAN between 6.2 and 6.4
Keep copy of config file for the current version
Log in at support.fortinet.com and select the Firmware Images Make sure to download the firmware corresponding to your device model
- Follow upgrade path
- Connect console to see consul errors
Upgrade best practice procedure

## Slide 105
FortiGates in the cluster must be the same model and have the same firmware installed. Cluster members must also have the same hardware configuration (such as the same number of hard disks) , also same licenses .
The following are critical components in an HA cluster:
Heartbeat connections: members will use this to communicate with each other. In general, a two-member cluster is most common. We recommend double back-to-back heartbeat connections.
Identical connections for internal and external interfaces: as demonstrated in the topology, we recommend similar connections from each member to the switches for the cluster to function properly.
best practices for general cluster operation:
Ensure that heartbeat communication is present.
Enable the session synchronization option
Monitor traffic flowing in and out of the interfaces.
HA Cluster

## Slide 106
HA Cluster

## Slide 107
FGCP provides failover protection in the following scenarios:
The active device loses power.
A monitored interface loses a connection.
Optionally, if an SSD fails, it can automatically fail over to a backup unit
To enable an SSD failure triggering HA fail over:
config system ha
set ssd-failover enable
end
HA Cluster: failover protection

## Slide 110
To upgrade the cluster firmware without interrupting communication, the following steps are followed. These steps are transparent to the user and the network, and might result in the cluster selecting a new primary unit.
The administrator uploads a new firmware image using the GUI .
The firmware is upgraded on the subordinate unit.
A new primary unit is selected from the upgraded subordinate.
The firmware is upgraded on the former primary unit.
Primary unit selection occurs , according to the standard primary unit selection process.
If all of the subordinate unit crash or otherwise stop responding during the upgrade process, the primary unit will continue to operate normally, and will not be upgraded until subordinate rejoins the cluster.
Upgrade with HA Cluster

## Slide 111
edit the first line as new model
For example : #config-version=FG201E-6.4.0-FW-build1579-200330:opmode=0:vdom=0:user=admin
Change the interfaces number if needed through notepad++
Migration config from model to model